## Slide 1
Part 1: MIPS Machine Instruction Set
一、https://www.icourse163.org/learn/HUST-1003159001
5.5、MIPS Instruction Overview 5.6、MIPS Instruction Details
二、Understand the sort.asm program and successfully run it in MARS
三、Referring to examples and the "MIPS32 Instruction Manual. PDF", translate the following 8 assembly instructions into 32-bit machine instructions
四、Convert sort.asm to sort.hex using MARS's Dump memory function
五、Self study Chapter 4.
lw $s4,128($s1)
slt $t0,$s3,$s4
100H:beq $t0,$0,sort_next (120H)
200H:bne $s0, $s1, sort_loop(220H)
addi $s1,$zero,28
sw $s3, 128($s1)
Add $s0,$zero,$zero
syscall

## Slide 2: MIPS Instruction format
OP=000000..111111;0..63
R-type instruction：OP=0,FUNCT=00-43
I -type instruction：OP=04..43
J -type instruction：OP=02,03

## Slide 3
No. | instruction | OpCode | FUNCT | function | tyoe
 |  | decimal | decimal |  | 
1 | ADD $rd,$rs,$rt | 0 | 32 | R[rd] = R[rs] + R[rt] | R
2 | SLT $rd,$rs,$rt | 0 | 42 | R[rd] = (R[rs] < R[rt]) ? 1 : 0 | R
3 | ADDI $rt,$rs,imm | 8 | X | R[rt] = R[rs] + SignExt{imm} | I
4 | LW $rt,imm($rs) | 35 | X | R[rt] = M[R[rs]+SignExt{imm}] | I
5 | SW $rt,imm($rs) | 43 | X | M[R[rs]+SignExt{imm}] = R[rt] | I
6 | BEQ $rs,$rt,imm | 4 | X | if(R[rs]==R[rt]) PC=PC+4+SignExt({imm,00}) | I
7 | BNE $rs,$rt,imm | 5 | X | if(R[rs]!=R[rt]) PC=PC+4+SignExt({imm,00}) | I
8 | SYSCALL | 0 | 12 | 停机 | R
examples：
①add $16,$0,$at
0,0,1,16,0,32
000000,00000,00001,
10000,00000,100000
0x0001,8020
②addi $s0,$0,-1
8,0,16,-1
001000,00000,10000
11111111,11111111
0x2010,ffff
General Register Number
8 machine instructions formats and functions

## Slide 5: Alu_op signal

## Slide 6
MIPS assembly simulation tool MARS. Note that the instruction memory (TEXT field) and data memory (DATA field) in the Haval structure are separated, and the starting address can be set；https://www.bilibili.com/video/BV1au411y7qq
code segment, Byte addr, instruction, assembler instruction
data segment Base Address offset Value sort.hex results
Message Value Display Method
Register alias， number ，value

## Slide 7
MARS、assembly、 go、 and step can debug and run instructions,Dump memory converts machine language programs in memory into a hexadecimal file *.hex, which can be loaded into Logisim's ROM for execution by the MIPS CPU (pay attention to the address range)

## Slide 8
What is the purpose of the MIPS assembly simulation tool MARS?
To debug and run instructions, and convert machine language programs into hexadecimal files
A
To design hardware for MIPS processors
B
To simulate the behavior of a multi-cycle MIPS CPU
C
To create graphical representations of MIPS instructions
D
提交
单选题
1分

## Slide 9
一、self-study https://www.icourse163.org/course/HUST-1205809816 Chapter 6
6.1、Single cycle MIPS framework
6.3、Single cycle MIPS CPU design (8 instructions)
二、Self study Chapter 5 P87-P90
三、Refer to the textbook 5.3 ,Single cycle MIPS processor design experiment in the template file, Verificate on TOUGE platform:
1、Single cycle hardwired controller
2、Single cycle MIPS (hard wired)
3、Run successful test program:sort.hex
四、Instruction Extension
Implement verification and instructions
Implement verification andi instructions
Implement verification j instruction
Other R、I、J type instructions can also be used
Part 2: Single cycle MIPS CPU

## Slide 10
点击添加文本
点击添加文本
点击添加文本
点击添加文本
4bit D Register：use device library and modification of device parameters，Be familiar with the use of CLK pin of sequential circuit.
4bit/16bit D Register
Current state
Next state

## Slide 11
点击添加文本
点击添加文本
点击添加文本
点击添加文本
1-digit decimal counter：FSM
FSM(Finite state machine)：Status register，State transition Combined circuit，Output Combined circuit；
16位D寄存器：熟悉时序电路的封装和调用
4、4bit/16bit D Register，BCD Counter，4-digit decimal counter
第一类，若输出逻辑只和状态有关而与输入无关，则称为Moore状态机
第二类，输出逻辑不仅和状态有关而且和输入有关系，则称为Mealy状态机
转 换
组合逻辑电路
组合逻辑电路
Moore状态机

## Slide 12: 计算机总结构图
ADD $rd,$rs,$rt
SLT $rd,$rs,$rt
ADDI $rt,$rs,imm
LW $rt,imm($rs)
SW $rt,imm($rs)
BEQ $rs,$rt,imm
BNE $rs,$rt,imm
SYSCALL
branch=Beq&Equal or Bne&~Equal
branch
次态
次态
次态

## Slide 14
Halt
branch=Beq&Equal or Bne&~Equal
branch

## Slide 15: Controller Design
using universal tables:
12 in: OP+FUNC
12 outputs: all output control signals
Combinational logic circuit Universal table only need 8 rows;

## Slide 16: MIPS CPU中的寄存器使用

## Slide 17: 8条指令指令格式和功能
opcode | 指令助记符 | RTL 功能描述 | 备注
0 (func:32） | add $rd, $rs, $rt | R[$rd] R[$rs]+R[$rt] | RegDest，Aluop=0101，Regwrite
0 (func:12) | syscall | 系统调用，PC不变 | Halt
0 (func:42) | slt $rd, $rs, $rt | R[$rd]R[$rs]<R[$rt] ，小于置1，有符号比较 | RegDest，Aluop=1011,Regwrite
04 | beq $rs, $rt, imm | If (R[$rs]=R[$rt]), PCPC+4+SignExt18b({imm左移2位}) | Beq，（imm是字地址，左移2位转换成字节地址）
05 | bne $rs, $rt, imm | If (R[$rs]!=R[$rt]), PCPC+4+SignExt18b({imm左移2位}) | Bne，（imm是字地址，左移2位转换成字节地址）
08 | addi $rt, $rs, imm | R[$rt] R[$rs]+SignExt16b(imm） | AluSrc, Aluop=0101，Regwrite
35 | lw $rt, imm($rs) | R[$rt] Mem (R[$rs]+SignExt16b(imm)之和右移2位) | AluSrc，Aluop=0101, MemToReg， Regwrite,（rs和imm都是字节地址，加法和要右移2位转换成字地址才能访问数据M）
43 | sw $rt, imm($rs) | Mem (R[$rs]+SignExt16b(imm)之和右移2位)R[$rt] | AluSrc,Aluop=0101, MemWrite，（rs和imm都是字节地址，加法和要右移2位转换成字地址才能访问数据M）
备注：跳转指令偏移地址imm求解公式：目标字节地址=当前地址+4+imm*4

## Slide 18
Single cycle MIPS CPU

## Slide 19: Controller circuit
这部分产生ALU_OP控制信号，
用三态门电路易于指令扩展
Input pin
Output pin

## Slide 20: The instructon decoder converts the OP field and FUNC field into an instruction tunnel: The ID use comparator. R_ Type=1 indicates a R-type instruction(except syscall).

## Slide 21: Load cs3410.jar，mips-probe.jar
cs3410.jar is an extended component library designed and shared by Cornell University for MIPS circuits, including the register group, ROM, RAM,ALU,display screen of the MIPS CPU

## Slide 22
What is the purpose of the cs3410.jar library in the MIPS CPU design?
To implement verification instructions
A
To provide an extended component library for MIPS circuits
B
To modify the instruction decoder
C
To add a MUX in front of the PC
D
提交
单选题
1分

## Slide 23: Instruction Extension 1、Implement verification and instructions 2、Implement verification andi instructions Modify the instruction decoder and ALU control logic， or add two rows in the universal table 3、Implement verification j instruction You must modify the instruction splitter, add the j instruction jump address circuit, j control signal, add a MUX in front of the PC, etc Other R、I、J type instructions can also be used
JMPADDR
JMPADDR= PC31..28 || instr_index || 00 PC=PC+4
PCBranch=PC+4+IMM16<<2
pc+4
PCBranch
instr_index